## Slide 1: Objective-Based Control for Intelligent Vehicles Under Uncertainty
James Fleming Loughborough University, UK
With thanks to my collaborators and colleagues:
Jakub Krol, Bani Anvari, Laura Justham, Mohammad Otoofi, Leo Laine, Roberto Lot, Neville Stanton, Xingda Yan, Leon Henderson, Qianyue Luo, Hui Zhang, Will Midgley

## Slide 2
Introduction:
  What do I mean by ‘objective-based’ control?
  Why do we care about uncertainty?
Some methodologies and case studies:
  Robust perception and sensing - road surface friction estimation from camera images
  Control to meet objectives despite uncertainty - robust and stochastic MPC
  What should the objectives be? – energy efficient ACC systems
Conclusion:
  Some closing thoughts and open research questions

## Slide 3: What is ‘objective-based’ control?
Methods that try to minimise/maximise an objective (cost or reward) function,
Can account for constraints, e.g. for collision avoidance (explicitly or via objective function)
Examples:
MPC and its variants (nonlinear, robust, economic…)
RL algorithms, like DDPG, TD3…
Control barrier functions resulting in QPs.... etc.
Why?
In complex situations, easier to specify goals, i.e. ‘what we want’ than ‘how to get it’
Can include ‘economic’ objectives, e.g. fuel/energy saving for the vehicle

## Slide 4: Motivation - why care about uncertainty?
Situations with limited visibility common while driving
Also changing weather conditions, reduced grip from tyres on road
If possible, should drive ‘defensively’ in these situations
How can we make controllers that do this ‘automatically’?
Some thoughts:
Need to make perception algorithms that are robust to reduced visibility
Design controllers that optimise/meet objectives despite this uncertainty
Ideally, perception algorithms should give some idea of the confidence of their detections/measurements
From Google Street View, ©Google, 2024
www.rac.co.uk/drive/advice/winter-driving/understanding-aquaplaning/ , ©RAC, 2024

## Slide 5: Framework: objective-based control with uncertainty
Can we do this with current methods?
Perception algorithms
Objective-function based controller
Autonomous vehicle
Control actions
State/parameter estimates
Confidence / uncertainty estimate

## Slide 6
Introduction:
  What do I mean by ‘objective-based’ control?
  Why do we care about uncertainty?
Some methodologies and case studies:
  Robust perception and sensing - road surface friction estimation from camera images
  Control to meet objectives despite uncertainty - robust and stochastic MPC
  What should the objectives be? – energy efficient ACC systems
Conclusion:
  Some closing thoughts and open research questions

## Slide 7: Uncertainty in perception
How to make perception methods that are robust to uncertainty, and give uncertainty estimates?
Classically - (extended) Kalman filter provides an uncertainty estimate via covariance matrix!
e.g. in mobile robotics EKF-based SLAM can give covariance matrices for position.
However, modern vehicles now have cameras, lidar…
These give complex, high-dimensional data, typically processed with ML - how to make perception robust and get uncertainty estimates?

## Slide 8: Case study: friction estimation
Recent collaboration with Volvo Trucks in Sweden
Estimate friction coefficient and surface type/condition​
  Combined regression and semantic segmentation problem, using a camera on the truck
  Semantic seg. commonly studied in the ML community, but to date few studies considering e.g. ice, snow, wet asphalt surfaces
  Would like a method lightweight enough to run in real time ~ 10Hz

## Slide 9: Data collection
Three test campaigns, carried out with assistance of Volvo Trucks in Sweden
Different surface types and conditions
1700 vehicle dynamic responses
GoPro camera
Data logger
  RT3000 data collection (acceleration, gyro)
  Truck CANbus signals

## Slide 10: Some examples of road scenes in dataset

## Slide 11: Deep learning Model for friction estimation
Conditional Variational Autoencoder (CVAE)
  ‘U-net’ encoder-decoder architecture, now popular in medical image segmentation, a generative model
  Learns low-dimensionality ‘latent spaces’ on which the data is approximately normally distributed – improve robustness
Friction estimation also from the CVAE
  Model trained to perform regression and classification of image pixels simultaneously
  Semantic understanding of surface type and condition (hopefully) benefits friction estimation

## Slide 12: Semantic segmentation: results

## Slide 13: Friction estimation: results
Performance for classification of surface type and friction estimation seems good
Snow is sometimes (~20%) misclassified as ice, but also hard to distinguish for humans.
Also tested the friction estimation performance using several ABS assisted stops on a test track in Sweden:

## Slide 14: Perception: how to get uncertainty estimates?
Overconfident
Well-calibrated
In principle, final ‘softmax’ layer gives a probability distribution – actually , the conditional distribution of the output given the data – i.e. quantifies the uncertainty
Much of the ML literature focuses on improving accuracy, not calibration...
For surface type and condition task, we are investigating how to improve calibration (currently overconfident)
i.e. a vector like:
How do we know this probability reported by the network is correct?

## Slide 15
Introduction:
  What do I mean by ‘objective-based’ control?
  Why do we care about uncertainty?
Some methodologies and case studies:
  Robust perception and sensing - road surface friction estimation from camera images
  Control to meet objectives despite uncertainty - robust and stochastic MPC
  What should the objectives be? – energy efficient ACC systems
Conclusion:
  Some closing thoughts and open research questions

## Slide 16: What control methods can account for uncertainty?
If we have uncertainty estimates, what (objective-function based) control methods can use them?
Nowadays, lots of robust and stochastic MPC methods are known!
  Stochastic methods can exploit knowledge of distribution of uncertainty
Why MPC? Can use model to predict effect of uncertain parameters, additive disturbances, etc – many types of system & uncertainty considered in literature
The above is also true for model-based RL, but no stability/performance guarantees
This isn’t a talk about MPC, so no gory details here, instead an example…

## Slide 17: Example: Robust MPC for vehicle platoon control
Collaboration with researchers at Beihang University
Acceleration and braking control of a vehicle platoon, with communication from leader and to followers
State constraints to avoid collisions between vehicles, each vehicle controlled by a tube MPC robust to additive disturbances
Also considered using an observer to estimate the disturbance

## Slide 18: Example: Robust MPC for vehicle platoon control
Simulation results showed that estimating the disturbance could improve performance
Some nice theoretical properties: recursive feasibility, stability, assuming the disturbance is bounded
Robust MPC:
With observer for disturbance:
*Luo, Q., Nguyen, A.T., Fleming, J. and Zhang, H., 2021. Unknown input observer-based approach for distributed tube-based model predictive control of heterogeneous vehicle platoons. IEEE Transactions on Vehicular Technology, 70(4), pp.2930-2944.

## Slide 19: Current EPSRC grant at LU
“Learning of safety critical model predictive controllers for autonomous systems” (EP/X015459/1)
Two current ‘objective-based’ approaches:
MPC (safety guarantees, but complex to design and implement, must redesign for every vehicle)
Reinforcement learning – (‘design’ is easy as it is automated, but no stability/feasibility guarantees)
Idea: Can we ‘reinforcement learn’ an MPC controller in an actor-critic framework?
Could give us the best of both worlds, i.e. a safe controller that is learned automatically from data.

## Slide 20
Introduction:
  What do I mean by ‘objective-based’ control?
  Why do we care about uncertainty?
Some methodologies and case studies:
  Robust perception and sensing - road surface friction estimation from camera images
  Control to meet objectives despite uncertainty - robust and stochastic MPC
  What should the objectives be? – energy efficient ACC systems
Conclusion:
  Some closing thoughts and open research questions

## Slide 21: What objectives would we like to optimise?
We can distinguish between:
Near-term, measurable control objectives, expressible as an objective function, that you might include e.g. in MPC or RL
Longer-term objectives that are wider requirements or goals for the system, but that don’t obviously relate to some objective function
Examples:
Safety / collision avoidance
Minimisation of journey time
Energy efficiency
User acceptance
Have beneficial effects on traffic
What objective functions should we specify for these?

## Slide 22: Case study: Energy-saving ACC systems
EPSRC project “Green Adaptive Control for Future Interconnected Vehicles”:
Aimed to develop energy saving optimal control methods for adaptive cruise control (eco-ACC) or autonomous vehicles, with good user acceptance.
Just driving more slowly is not an option (poor user acceptance). We would like to account for preferences on speed, acceleration, following distances.
Example: How to decelerate before stop signals?
Potential impact:
Combustion engine vehicles: “The difference in fuel consumption and emissions due to driving behaviour can be up to 25% in urban areas” (UDRIVE project, D45.1)
Electric vehicles: Experimental studies on eco-driving assistance have shown ~15% reduction in energy usage (e.g. Dib et al, 2014, “Optimal energy management for an electric vehicle in eco-driving applications”, Control Engineering Practice)

## Slide 23: Energy-saving ACC as an optimal control problem
Driving to minimise energy loss is an optimal control problem (OCP), can solve it numerically to control vehicle
We add a term to blend energy-saving behaviour with typical human behaviour – for better user acceptance.
For ACC, it turns out that human car-following behaviour is well-represented by a cost function of the form*:
Energy usage
Can implement in practice using economic / nonlinear MPC
Useful: avoids unnatural behaviour, improves user acceptance compared to minimising energy
*Fleming et al, 2020. “Incorporating driver preferences into eco-driving assistance systems using optimal control”. IEEE Trans. on Intelligent Transportation Systems.
Human preferences

## Slide 24: Results: Energy saving ACC
Stop signal example: Variable coasting behaviour
Human preferences
Real-world car-following data example:
(true energy-minimisation behaviour is unnatural!)

## Slide 25: Case study: effect on other traffic?
What is the wider effect of driving like this on other traffic?
Recent results of a collaboration with researchers at UCL using SUMO microscopic traffic simulation:
Also saves energy for other vehicles following ours,
(e.g. by coasting down before stop signals)
no/negligible increase in travel times.

## Slide 26
Introduction:
  What do I mean by ‘objective-based’ control?
  Why do we care about uncertainty?
Some methodologies and case studies:
  Robust perception and sensing - road surface friction estimation from camera images
  Control to meet objectives despite uncertainty - robust and stochastic MPC
  What should the objectives be? – energy efficient ACC systems
Conclusion:
  Some closing thoughts and open research questions

## Slide 27: Framework: objective-based control with uncertainty
Can we do this with current methods?
Perception algorithms
Objective-function based controller
Autonomous vehicle
Control actions
State/parameter estimates
Confidence / uncertainty estimate

## Slide 28: Conclusions and current challenges
ML models for perception can estimate probabilities of states/parameters
  But… many methods aim for high accuracy, not good calibration of probabilities
There are now lots of methods for stochastic/robust MPC
  But… complex to implement, takes expert knowledge to design for each vehicle
Using economic objectives, controllers can save energy / increase range
  Can we also design objective functions that promote other goals, such as user acceptance, improved traffic flow, etc?